## Slide 1: Estimating crowd on a bus using Wi-Fi/Bluetooth
Anil Yelam
Notes: Warning: graphic

## Slide 2: Motivation
Inform bus stops further ahead on the route
Tracking crowd transit patterns
  Better scheduling of buses during times of day
  Improved efficiency
  Optimal bus routes
Notes: 201 was mostly empty except at few bus stops around UCSD, a better route would improve service efficiency.

## Slide 3: Related work
Surprisingly, no work directly on this problem (to the best of my knowledge)
  Other simpler and more accurate solutions like sensors installed at door?
    They could be expensive or complex to install? (Not sure, but I hope so!)
  Interesting problem nevertheless!
One paper on Wi-Fi sniffer based statistics collection at bus stops
  Does not account for mac address randomization
Notes: http://www.arpnjournals.org/jeas/research_papers/rp_2016/jeas_0616_4532.pdf

## Slide 4: Smartphones as proxies
Have you seen anyone without a smartphone, or a smartphone without Wi-Fi?
Not like localization through human detection
  Cannot actively localize
  Requires complex setup of access points
  Need lots of training data
  Definitely not going to beat “sensors at doors” solution!

## Slide 5: How to count devices *passively*
Using Wi-Fi
  Probe requests
Using Bluetooth
  Responses to Bluetooth scans

## Slide 6: Challenges with Wi-Fi
Could be turned off, although assumption is that it’s usually rare
  Exceptions: Both my roommates
No access points – no active data traffic
  Probe requests to the rescue!
Excluding outside traffic
  Filtering out the short-lived traffic

## Slide 7: MAC address randomization
High adoption
Insight: Probe packets still carry certain signature
  Tagged parameters
  Sequence number

## Slide 8: Challenges with Bluetooth
Main issue: Not always ON
  Much less than Wi-Fi
Involves active responses?
Otherwise, much easier. No randomization!

## Slide 9: Test data & the ground truth
Few rides on 201 route
Bluetooth data: Bluetana
Wi-Fi data: Wireshark on Mac

## Slide 10: Started with Bluetooth
Scans every 10-15 seconds
  Should have used every second scanning
Almost 70% is external traffic – doesn’t last more than a minute

## Slide 11: Dataset 1

## Slide 12: Dataset 2

## Slide 13: Over to Wi-Fi
More excited about results from Wi-Fi
Looking into the data, didn’t get to clustering yet
Hoping it’ll give better estimate

## Slide 14: Dataset 1

## Slide 15: Dataset 2

## Slide 16: Dataset 2

## Slide 17: Conclusion
Work on Wi-Fi data
Look a bit more into Bluetooth results
Will show you any interesting results

## Slide 18: Thank you!